## Slide 1
COMPUTER NETWORKS
Computer Networks
Fundamentals, Protocols, Architecture & Modern Networking
Prepared by: ____________________
Course: Computer Networks
Date: ____________________

## Slide 2
GETTING STARTED
Introduction to Computer Networks
What is a Computer Network?
A collection of interconnected devices — computers, servers, mobile phones, routers, and switches — that communicate with each other to share data, resources, and services.
Key Components
1
Sender
2
Receiver
3
Transmission Medium
4
Network Devices
5
Protocols
Why Networks Are Important
✓
Share files, printers, and applications
✓
Enable email, messaging, and video conferencing
✓
Provide access to the internet and cloud services
✓
Support centralized data storage and management
✓
Improve collaboration and productivity
Real-World Examples
Home Wi-Fi network
College campus network
Banking network (ATMs & servers)
Cloud data centers (AWS, Azure, GCP)
COMPUTER NETWORKS
02

## Slide 3
CLASSIFICATION
Types of Computer Networks
Based on Geographical Area
Type | Coverage | Example
PAN | Few meters | Bluetooth, smartwatch
LAN | Building or office | College lab
MAN | City-wide | Municipal fiber network
WAN | Country or global | The Internet
PAN — Personal Area Network
• Connects personal devices
• Bluetooth, USB, NFC, infrared
• Low power consumption
LAN — Local Area Network
• 100 Mbps to multi-Gbps speeds
• Privately owned
• Schools, offices, homes
WAN — Wide Area Network
• Connects LANs across distances
• Leased lines, fiber, satellite
• Internet is the largest WAN
Advantages of Networking
Resource sharing
Faster communication
Centralized backup
Cost reduction
COMPUTER NETWORKS
03

## Slide 4
REFERENCE ARCHITECTURE
OSI 7-Layer Model
7
Application
User services
6
Presentation
Translation, encryption, compression
5
Session
Establishes and manages sessions
4
Transport
Reliable delivery
3
Network
Routing and logical addressing
2
Data Link
Framing and MAC addressing
1
Physical
Transmission of bits
Easy Memory Trick
“All People Seem To Need Data Processing”
Layer Cheat-Sheet
• Physical: cables, connectors, signals
• Data Link: Ethernet, switches, MAC
• Network: IP addressing & routing
• Transport: TCP and UDP
• Application: HTTP, FTP, SMTP, DNS
Standardizes communication • Simplifies troubleshooting • Enables multi-vendor interoperability
COMPUTER NETWORKS
04

## Slide 5
PROTOCOL SUITE
TCP/IP Model & Comparison
Application
App + Presentation + Session
Transport
Transport
Internet
Network
Network Access
Data Link + Physical
Major Protocols
Application: HTTP/S, FTP, SMTP, DNS, DHCP Transport: TCP (reliable), UDP (fast) Internet: IPv4, IPv6, ICMP, ARP
TCP vs UDP
TCP | UDP
Reliable | Faster
Ordered delivery | No guarantee
Error recovery | Minimal overhead
Used for web, email | Used for streaming, gaming, VoIP
Why TCP/IP Is Dominant
✓
Open standard, not vendor-specific
✓
Scalable from small to huge networks
✓
Works across heterogeneous networks
✓
Backbone of the modern Internet
TCP/IP is the practical, layered rulebook every device on the Internet follows to package, address, and deliver data.
COMPUTER NETWORKS
05

## Slide 6
PHYSICAL LAYER
Transmission Media
Guided Media
T
Twisted Pair
Most common Ethernet cable; cheap & easy to install
C
Coaxial Cable
Better shielding; used in cable TV & broadband
F
Optical Fiber
Light signals; very high bandwidth, long distance
Unguided Media
R
Radio Waves
Wi-Fi, Bluetooth
M
Microwaves
Satellite & cellular communication
I
Infrared
Remote controls, short range
Comparison
Medium | Speed | Cost | Distance
Twisted Pair | Medium | Low | Short
Coaxial | Medium | Medium | Medium
Fiber Optic | Very High | Higher | Very Long
COMPUTER NETWORKS
06

## Slide 7
INFRASTRUCTURE
Network Devices & Switching
Important Networking Devices
H
Hub
Broadcasts to all ports; no intelligence; mostly obsolete
S
Switch
Uses MAC addresses; sends only to destination port; reduces collisions
R
Router
Connects different networks; uses IP addresses; finds best packet path
A
Access Point
Provides wireless connectivity; bridges Wi-Fi to wired LAN
Switching Techniques
Circuit Switching
Dedicated path for the session; used in traditional telephone systems.
Packet Switching
Data is divided into packets for efficient bandwidth usage; used by the Internet.
Packet Switching Advantages
• Better resource utilization
• Supports multiple users simultaneously
• More fault tolerant
COMPUTER NETWORKS
07

## Slide 8
NETWORK LAYER
IP Addressing and Routing
IPv4
32-bit
e.g. 192.168.1.10
~4.3 billion addresses
IPv6
128-bit
e.g. 2001:db8::1
Huge address space, solves IPv4 exhaustion
Subnet Mask
Determines the Network portion and Host portion of an address.
IP: 192.168.1.25 Mask: 255.255.255.0
Routing
Routers maintain routing tables to forward packets toward their destination.
Static Routing
Manually configured; suitable for small networks.
Dynamic Routing
Automatically updates routes. Protocols: RIP, OSPF, EIGRP, BGP.
Default Gateway: the router that forwards packets to other networks or the Internet.
COMPUTER NETWORKS
08

## Slide 9
PROTECTION
Network Security
Common Threats
Unauthorized access
Data theft
Malware
Ransomware
Denial-of-Service attacks
Security Mechanisms
F
Firewall
Filters traffic & enforces security policies
A
Antivirus
Detects & removes malicious software
E
Encryption
Converts data into unreadable form
V
VPN
Secure encrypted tunnel for remote access
CIA Triad
C
Confidentiality
I
Integrity
A
Availability
Best Practices
Strong passwords • Multi-factor authentication • Keep software updated • Use HTTPS • Regular backups
COMPUTER NETWORKS
09

## Slide 10
LOOKING AHEAD
Emerging Technologies & Conclusion
C
Cloud Networking
AWS, Azure, Google Cloud — virtual networks & scalable infrastructure
S
SDN
Separates control plane from data plane for centralized, flexible management
I
IoT
Billions of connected sensors across homes, healthcare, agriculture, industry
5
5G Networks
Very high data rates & low latency for autonomous vehicles, AR/VR, IoT
Key Takeaways
✓
Networks enable communication and resource sharing
✓
OSI and TCP/IP models provide structured communication
✓
Switches and routers are core networking devices
✓
IP addressing and routing allow global connectivity
✓
Network security is essential for protecting systems
✓
Cloud, SDN, IoT & 5G are shaping the future
COMPUTER NETWORKS
10

## Slide 11
THANK YOU
Thank You
Questions & Discussion
Contact: ____________________
Email: ____________________